|  | SAFETY DATA SHEET MINERAL FERTILIZERS CONTAINING SUPERPHOSPHATE |
| --- | --- |

SECTION 1: Identification of the substance/mixture and of the company/undertaking

  - Product identification

Trade name: BORÓWKA (BLUEBERRY) IGLAK (PINE TREE) JESIENNY (AUTUMN) JESIENNY UNIWERSALNY (UNIVERSAL AUTUMN) LUBOFOS 10 LUBOFOS 12 LUBOFOS 5-10-25 LUBOFOS CHLORIDE FREE FERTILIZER 3.5-10-15 LUBOFOS PK LUBOFOS PKMg LUBOFOS POD ZIEMNIAKI (LUBOFOS FOR POTATOES) LUBOFOSKA LUBOFOSKA 0-12-24 LUBOFOSKA 3.5-10-20 LUBOFOSKA 3.5-11-17 LUBOFOSKA 5-10-15 LUBOFOSKA CHLORIDE FREE FERTILIZER 3.5-10-15 LUBOPLON 0-10-30 LUBOPLON 0-20-30 PKMg13 RODODENDRON, AZALIA, WRZOS (RHODODENDRON, AZALEA, HEATHER) SUPERFOSFAT MAGNEZOWY (MAGNESIUM SUPERPHOSPHATE) TRUSKAWKA (STRAWBERRY) Mineral fertilizers are mixtures containing the following substances: calcium phosphate and ammonium phosphate, magnesite, ammonium sulphate, potassium sulphate, kieserite, dolomite, borax, other

  - Relevant identified uses of the substance or mixture and uses advised against

Short description of identified use Field of application Process category Product category Final use Sampling, loading, transfer, transfer from/to small containers, storage, packing at places intended and not intended for this purpose. Industrial use SU3 PROC 8a PROC 8b PROC 9 PC12, PC20 formulation , industrial Preparation of mixtures SU3 PROC2 PROC3 PROC5 PC12 formulation Sampling, loading, transfer, transfer from/to small containers, storage, packing at places intended and not intended for this purpose. Professional use SU22 PROC 8a PROC 8b PROC 9 PC12 professional Professional use of fertilizers containing superphosphate - sowing in field and agricultural cultivation, foliar feeding on fields, fertigation. SU22 PROC 8a PROC 8b PROC 2 PC12 professional Use by consumers of fertilizers containing superphosphate - sowing in house gardens (solid and liquid fertilizers) and outdoor use SU21 - PC12 consumer Use advised against: None

  - Details of the supplier of the safety data sheet

LUVENA S.A. ul. (street) Romana Maya 1 62-030 Luboń tel. (061) 8900100 fax.(061) 8900400 e-mail of the person responsible for preparation of this safety sheet danuta.rybarczyk@luvena.pl

  - Emergency phone numbers

Gdańsk 058 3492831 Cracow 012 6471105; 012 6831134; 012 6831300 Lublin 081 7408983 Łódź 042 6314767 Poznań 061 8476946 0618481011 ext. 265 Rzeszów 017 866 4406 Sosnowiec 032 2661145; 032 2660885 ext.130 Tarnów 014 6299588 Warsaw 022 6190897; 022 6196654 Wrocław 071 3433008; 071 3427021; 071 7890214

SECTION 2: Hazards identification

  - Classification of the substance or mixture

according to Directive 67/548/EEC according to EC Regulation No. 1272/2008 (CLP) Xi Irritant R41 Risk of serious damage to eyes Serious damage to eyes, cat. 1 H318 Causes serious damage to eyes

  - Labelling elements

Pictogram: GHS05 Warning: DANGER Identification: CAS 8011-76-5 Description: contains superphosphate Phrases describing the type of risk: H318 Causes serious damage to eyes Phrases indicating precautionary measures: P280 Use protective gloves/ protective clothing/ eyes protection/ face protection P305+P351+P338 IN CASE OF CONTACT WITH EYES: Carefully rinse with water for several minutes. Remove contact lenses, if any, and are easy to remove. Continue rinsing. P 310 Immediately consult POISONING TREATMENT CENTER or a physician.

  - Other risks

Mixtures of inorganic compounds, therefore it is not assessed as PBT and vPvB.

SECTION 3: Composition / information on ingredients

  - Substances

| Not applicable - mixture safety data sheet |  |
| --- | --- |

  - Mixtures

The mixture contains the following dangerous components: Superphosphate Concentration: 15-70 % Type of substance: multicomponent substance Identification numbers: CAS No. EC No. Index No. 8011-76-5 232-979-5 - IUPAC name: Superphosphate Chemical formula: not determined Registration No.: 01-2119488967-11 Classification: according to Directive 67/548/EEC refers to 100% of the substance according to EC Regulation No. 1272/2008 (CLP) refers to 100% of the substance Xi Irritant R41 Risk of serious damage to eyes Serious damage to eyes, cat. 1 H318 Causes serious damage to eyes

SECTION 4: First aid measures

  - Description of first aid measures

4.1.1. Inhalation. If undesirable symptoms occur (e.g. dizziness, sleepiness and irritation of respiratory system) take the injured person out of the contaminated environment to fresh air. If the person does not breathe, apply artificial respiration and in case of breathing difficulties, supply oxygen and consult a physician. Immediately consult a physician in case of intensive inhalation of the dust. 4.1.2. Skin contact Wash the contaminated skin with copious amount of water with soap for at least 15 minutes, removing thoroughly the contaminated clothes and shoes. Consult a physician in case the irritation lasts. 4.1.3. Eyes contact Immediately rinse eyes with copious amount of running water for at least 15 minutes, lifting the upper and lower eyelid from time to time. Remove contact lenses, if any, and are easy to remove. Continue rinsing. Immediately consult POISONING TREATMENT CENTER or a physician. 4.1.4 Digestion If the injured person feels unwell, consult a physician. Wash the mouth out with large quantity of water and give plenty of water to drink. Do not provoke vomiting. Do not administer anything orally, if the injured person is unconscious. If the symptoms do not abate, provide medical assistance.

  - The most important severe and delayed symptoms and effects of exposure

Severe effect: irritant to eyes Long-term effect: not known

  - Indications concerning all immediate medical assistance and special handling of the injured

Inhalation of gases produced during fire and thermal decomposition, containing phosphorus and sulphur oxides, may have irritating and caustic effect on respiratory system. Effect on lungs may be delayed.

SECTION 5: Fire-fighting measures

  - Fire extinguishing measures

Fire in the environment should be extinguished with the use of extinguishing measures as appropriate for the burning materials.

  - Special risks related to the substance or mixture

During fire there may be produced hazardous gases or vapours: phosphorus and sulphur oxides

  - Information for a fire brigade

No special measures necessary. In case of fire wear personal breathing apparatus and protective clothing. Avoid inhalation of vapours, stand on the leeward side. Ensure maximum ventilation - open windows and doors.

SECTION 6: Accidental release measures

  - Personal precautions, protective equipment and emergency procedures

Avoid creation of dusts and prevent spreading by the wind. Provide adequate ventilation. Avoid contact with eyes, skin and clothes. Use appropriate protective equipment: protective clothing, dust masks, protective gloves and glasses

  - Environmental precautions

Avoid contamination of water, water intakes or sewers. In case of accidental pollution, notify appropriate authorities.

  - Methods and materials preventing spreading of the contamination and used for removal of the contamination

Collect the spilled material and place it with appropriate containers marked with the labels: for recycling or neutralisation. Wash off with copious amounts of water. Avoid dust clouds and spreading by the wind.

  - Reference to other sections

Personal protective measures - see section 8 Handling of waste - see section 13.

SECTION 7: Handing and storage of substances and mixtures

  - Precautions concerning safe handling

Avoid contact with eyes, skin and clothes. Avoid excessive dust formation. Protect from moisture. Avoid contamination with flammable materials (e.g. diesel fuel, grease, etc.) and/or other incompatible materials - see 10.5. Thoroughly clean all equipment prior to maintenance and repairs. Do not eat, drink or smoke during handling the mixture. Wash yourself thoroughly after work.

  - Condition of safe storage including information on all incompatibilities

Fertilizer should be stored in clean and dry storage facilities. It is also accepted storage in packages under station roof and on storage areas with hardened or ground pavement covered with protective material, e.g. foil, canvas sheet. Bulk fertilizer should be stored in piles or between division walls in order to protect it from mixing with other substances. Product should be kept out from direct sun, moisture and water and incompatible materials: alkalies, urea, ammonium nitrate (see 10.5)

  - Special final uses

At present there are no recommended rules of behaviours resulting from special final uses of the product

SECTION 8: Exposure control / personal protective measures

  - Control parameters

Total dust NDS 10 mg/m3 Methods of exposure assessment: PN-Z-04008-7:2002 PN-Z-04008-7:2002/AZ1:2004 Sampling: dust and chemical air pollution. Dosimetric and stationary method PN-91/Z-04030.05 Concentration of total dust Range: (0.15 - 25.0) mg/ m3 Filtration and weighing method PN-91/Z-04030.06 Concentration of respirable dust Range: (0.15 - 16.6) mg/ m3 Filtration and weighing method Acceptable exposure limits for SSP: Ways of exposure Highest acceptable level of human exposure DNEL Worker Society in general Oral (1) not applicable 2.1 mg/kg of body mass/day Through skin (1) 17.4 mg/kg of body mass/day 10.4 mg/kg of body mass/day Through inhalation (1) 3.1 mg/m3 0.9 mg/m3 As severe toxic risk leading to classification and labelling of the substance has not been established, during long-time exposure DNEL is sufficient to ensure that the effects of severe exposure to the substance do not exist.

  - Exposure control

Exposure control technical measures Avoid high dustiness. Provide adequate ventilation as required. Moreover, following the good industrial practice during storage and handling of the mixture one may use the equipment for eyes rinsing and safety shower. Personal protective measures In case insufficient ventilation use respiratory system protection (dust mask or respirator with appropriate filters, e.g. EN 143, 149, Filter P2, P3). Use protective gloves (e.g. plastic, rubber, leather) in case of long-lasting contact with the product. Protect eyes using protective gloves or face shield. Use protective clothing. When using the product over long periods of time, use appropriate personal protective measures. It is recommended to apply basic hygiene principles when handling chemicals, i.e.: wash your hands, forearms and face thoroughly after completed work and before eating, smoking and using WC. Use appropriate techniques to dispose of potentially contaminated clothes. Environmental precautions Disposed the water used for rinsing according to the local and national regulations.

SECTION 9 : Physical and chemical proprieties

  - Information on basic physical and chemical proprieties

Appearance Solid body in form of a dust and pellets Odour: No odour Odour threshold No data pH Depending on the type of fertilizer Melting / freezing point Does not reach melting point, decomposition (on the basis of the main components) Starting boiling point and range of boiling temperatures Does not reach boiling point, decomposition Flash point Insignificant, mixture of inorganic compounds, non-flammable Evaporation rate No data Flammability (of the solid body, gas) Non-flammable mixture (on the basis of the composition and components) Upper / lower flammability limit or upper / lower explosiveness limit Not applicable Vapour pressure Detail information for Superphosphate: 8.4x10-7 Pa @ 20°C (OECD 104, EC A.4) Vapour density No data Bulk density 900-1100 kg/m3 Solubility Water soluble, may create water slurries N-octanol / water partition coefficient Not applicable, mixture of inorganic compounds Autoignition point None Breakdown temperature No data Viscosity Not applicable; solid mixture Explosive properties No properties (on the basis of the composition) Oxidizing properties No properties (on the basis of the composition and experience in use)

  - Other information

None

SECTION 10: Stability and reactivity

  - Reactivity

Product stable under recommended storage and handling conditions (see Section 7).

  - Chemical stability

Product stable under recommended storage and handling conditions (see Section 7).

  - Possible dangerous reactions

Dangerous reactions may occur during heating - decomposition products, see item 10.6

  - Conditions to avoid

Heating, contact with alkalies

  - Incompatible materials

Alkalies, ammonium nitrate

  - Hazardous decomposition products

Under normal storage and use conditions hazardous decomposition products should not be created. Creation of poisonous gases is possible during heating or in case of fire: e.g. phosphorus oxides (e.g. P2O5), sulphur oxides (SOx), ammonia, chloride, fluoride, hydrogen chloride

SECTION 11: Toxicological information

  - Information on toxicological effects

Health results, short-term exposure, data for superphosphate: Acute toxicity: LD50 (orally) > 2000 mg/kg (OECD 425 test material: diammonium phosphate) LD50 (skin) > 5000 mg/kg (OECD 402 test material : diammonium phosphate) LC50 (inhalation) > 5 mg/l (OECD 403 test material: diammonium phosphate) Effect: Skin irritation: does not irritate (OECD 404 test material: diammonium phosphate) Eye irritation: caustic effect (OECD 405, EC B.5) Skin sensitization: does not sensitize (OECD 429, EC.42 test material: diammonium phosphate) Other effects: Health results, long-term exposure, data for superphosphate: NOAEL orally 28 days: 250 mg/kg of body mass/day (OECD 422 test material: concentrated superphosphate TSP) Mutagenicity: negative (OECD 471 test material: concentrated superphosphate TSP) negative (OECD 473) negative (OECD 476 test material: diammonium phosphate) Effect on reproductiveness: orally NOAEL 750 mg/kg of body mass/day (OECD 422 test material: concentrated superphosphate TSP) Carcinogenicity: no data STOT one-time exposure: not applicable STOT multi-time exposure: not applicable Exposure by aspiration: no data

SECTION 12: Ecological information

  - Toxicity

Acute toxicity indicator Detail information for superphosphate LC50 (fish, 96 h) >85.9 mg/l (OECD 203, test material: diammonium phosphate) EC50 (daphnia, 72 h) 1790 mg/l EC50 (algae, 72 h) > 87.6 mg/l (OECD 201, test material: concentrated superphosphate TSP) EC50 (active deposit, 3 h) >100 mg/l, NOEC: 100 mg/l (OECD 209, EC C.11)

  - Durability and degradability

Nitrogen undergoes natural nitrification or denitrification cycle, producing nitrogen or nitrogen oxides. Phosphates are transformed into calcium, iron and aluminium phosphates, or combine with the organic matter of the soil. Potassium is absorbed by clay soils or exists in ionic form in soil solutions. Product should not be released to sewage in large quantities, as it may cause eutrophication of closed water regions.

  - Bioaccumulation potential

Due to the properties of inorganic compounds - the potential is low

  - Mobility in soil

Good solubility in water. Ammonium ion is absorbed by soil particles. Phosphates are transported in the soil for a short time and then are immobilized in the soil. Potassium ion is absorbed by clay soils. In light soils potassium may be washed out.

  - Results of evaluation of PBT and vPvB

Mixtures of inorganic compounds, therefore it is not assessed as PBT and vPvB.

  - Other adverse effects

None

SECTION 13: Disposal considerations

  - Neutralization of waste

According to local and national regulations the waste is disposed by deposition or combustion. Prevent the substances from penetration to watercourses. Biodegradation control is possible under the process of waste water treatment. Wastes and used packaging should be delivered to a company dealing with waste management. Waste code number 02 01 08 Agrochemical waste containing hazardous substances, including crop protection chemicals of 1st and 2nd class toxicity (very toxic and toxic) Packaging code number: 15 01 10 Packaging containing residues of hazardous substances or contaminated with such.

SECTION 14: Transport information

  - UN number

It is not classified as hazardous product according to ADR/RID regulations

  - UN proper shipping name

It is not classified as hazardous product according to ADR/RID regulations

  - Transport hazard classes

It is not classified as hazardous product according to ADR/RID regulations

  - Packaging group

It is not classified as hazardous product according to ADR/RID regulations

  - Environmental hazard

Not labelled as dangerous for the environment

  - Special precautionary measures for the user

None

  - Shipping in bulk according to the Appendix II to the convention MARPOL 73/78 and IBC code

not applicable

SECTION 15: Regulatory information

  - Safety, health and environmental regulations/legislation specific for the substance or mixture

Acts Journal of Laws 2009 No. 152, item 1222 Announcement of the Speaker of the Sejm of the Republic of Poland of 27 August 2009 on publication of the uniform text of the act on chemical substances and preparations. Journal of Laws 2001 No. 62 item 628, as amended Act of 27 April 2001 on wastes Journal of Laws of 2001 No. 63, item 638, as amended Act of 11 May 2001 on packaging and packaging wastes Regulations - Classification Journal of Laws 2003 No. 171, item 1666, as amended Regulation of the Minister of Health of 2 September 2003 on the criteria and method of classification of chemical substances and preparations Regulations - Labelling Journal of Laws 2009 No. 53, item 439 Regulation of the Minister of Health of 5 March 2009 on labelling of packages of hazardous substances and hazardous preparations and some chemical preparations Journal of Laws 2010 No. 125 item 851 Regulation of the Minister of Health of 16 June 2010 on the method of labelling places, pipelines and containers and tanks used for storage or containing hazardous substances or hazardous preparations Journal of Laws 2010 No. 83 item 544 Regulation of the Minister of Health of 29 April 2010 on the types of hazardous substances and hazardous preparations whose packaging is provided with closures making it more difficult to open by children and hazard warning which could be felt by touch. Regulations - Limitations and bans Journal of Laws 2004 No. 168 item 1762, as amended Regulation of the Minister of Economy and Labour of 5 July 2004 on limitations, bans or conditions of production, turnover or use of hazardous substances and hazardous preparations and products containing the same Regulations - Occupational Health and Safety Journal of Laws 2004 No. 280 item 2771 Regulation of the Minister of Health of 1 December 2004 on substances, preparations, agents or manufacturing process having cancerous or mutagenic effect in labour environment. Journal of Laws 2005 No. 11, item 86, as amended Regulation of the Ministry of Health of 30 December 2004 on occupational health and safety related to chemical agents present at the place of work Journal of Laws 2002 No. 217 item1833, as amended Regulation of the Minister of Labour and Social Policy on the maximum acceptable concentration and intensity of agents hazardous to health in the work environment Journal of Laws No. 7 item 59, as amended Regulation of the Minister of Economy and Labour of 14 January 2004 on occupational health and safety at production and storage of gases, filling containers with gases and use and storage of carbide (). Regulations - Environmental protection Journal of Laws 2001 No. 112 item 1206 Regulation of the Ministry of the Environment of 27 September 2001 on waste catalogues EC Regulations Official Journal of the EU 2007 L 136 corrigendum to Official Journal of the UE 2006 L 396 Corrigendum to the Regulation (EC) No 1907/2006 of the European Parliament and of the Council of 18 December 2006 concerning the Registration, Evaluation, Authorisation and Restriction of Chemicals (REACH), establishing a European Chemicals Agency, amending Directive 1999/45/EC and repealing Council Regulation (EEC) No 793/93 and Commission Regulation (EC) No 1488/94 as well as Council Directive 76/769/EEC and Commission Directives 91/155/EEC, 93/67/EEC, 93/105/EC and 2000/21/EC Official Journal of the EU 2008 L 354 Regulation (EC) No 1336/2008 of the European Parliament and of the Council of 16 December 2008 amending Regulation (EC) No 648/2004 in order to adapt it to Regulation (EC) No 1272/2008 on classification, labelling and packaging of substances and mixtures (1) Official Journal of the EU 2008 L 353 Regulation (EC) No 1272/2008 of the European Parliament and of the Council of 16 December 2008 on classification, labelling and packaging of substances and mixtures, amending and repealing Directives 67/548/EEC and 1999/45/EC, and amending Regulation (EC) No 1907/2006 (1) Official Journal of the EU 2009 L 235 Commission Regulation (EC) No 790/2009 of 10 August 2009 amending, for the purposes of its adaptation to technical and scientific progress, Regulation (EC) No 1272/2008 of the European Parliament and of the Council on classification, labelling and packaging of substances and mixtures (1) Official Journal of the EU 2008 L204 Regulation (EC) No 689/2008 of the European Parliament and of the Council of 17 June 2008 concerning the export and import of dangerous chemicals Official Journal of the EU L 6/1 of 9.1.2010 Commission Regulation (EU) No 15/2010 of 7 January 2010 amending Annex I to Regulation (EC) No 689/2008 of the European Parliament and of the Council concerning the export and import of dangerous chemicals Official Journal of the EU L 60/5 z 10.3.2010 Commission Regulation (EU) No 196/2010 of 9 March 2010 amending Annex I to Regulation (EC) No 689/2008 of the European Parliament and of the Council concerning the export and import of dangerous chemicals Other Classification of dangerous goods according to ADR Agreement and RID Regulations Journal of Laws No. 164, item 1115 Regulation of the Minister of Health of 1 September 2010 on the mode of chemical substance, chemical preparation or product recall and method of their storage

  - Chemical Safety Assessment

According to Article 14 of REACH there have been conducted Chemical Safety Assessment for superphosphate and borax

SECTION 16: Other information

Training: Employees should be instructed within the scope of proper handling of the preparation. One should read the safety data sheet before use of the preparation. Limitations of use: none. Data sources: Legal regulations listed under item 15.1, Chemical Safety Report for superphosphate, eSDS prepared by FARM consortium for superphosphate Amendments made: not applicable, first issue of the MSDS

This MSDS is consistent with Appendix II to REACH amended by the (EU) Commission Regulation No. 453/2010 of 20 May 2010. All data contained therein are consistent with the present knowledge and our experience. Safety data sheet is a description of products as regards safety requirements. It is not the intention of our data to ensure product's properties.